## Slide 1
GeoCost - assessment of groundworks and foundation reinforcement costs for buildings
Mats Öberg/Jim Hedfors
GIS Development, SGI
ESRI User Conference, San Diego, July 12, 2017
(3:15 PM - 4:30 PM; Paper #: 86, Room 24 A)

## Slide 2
Sweden, covered by ice ~20.000 years ago…
https://commons.wikimedia.org/wiki/File:Weichsel-W%C3%BCrm-Glaciation.png#/media/File:Weichsel-W%C3%BCrm-Glaciation.png
http://www.geus.dk/viden_om/voii/ilulissat-uk/voii03-uk.html
This has shaped soil formation of Scandinavia, Canada etc - important for foundation reinforcement methods
S W E D E N
SGI is a government agency and research institute.
Mission to reduce the risks of landslides and erosion

## Slide 3
What is GeoCost?
An ArcGIS-based tool (Models) for estimating foundation reinforce-ment costs in municipal develop-ment (and infrastructure*)
GIS + Geotechnical engineer
http://www.swedgeo.se/geokalkyl/
Large savings can be made by placing constructions in areas with the most favorable geotechnical conditions.
Quickly calculates (alternative) costs for cut/fill, foundation reinforcement etc. Detailed elevation and soil data is used.
Financed by the Swedish Government
*) Also used by Swedish Transport Administration

## Slide 4
Illustration of foundation reinforcement cost per m2 and suggested reinforcement method
Also summaries of TOTAL cost and TOTAL cut/fill volumes

## Slide 5
System workflow
Skills requirements:
ArcGIS operator
Geotechnical engineer
Software requirements:
ArcGIS Desktop 10.2+
3D-analyst
Microsoft Excel 2010+
Geoteknik
GIS
Geotechics

## Slide 6
Prepare input data
Calculate foundation depth & cut/fill volumes
Calculate costs/
generate 3D scene
Calculate foundation reinforcement methods (piles etc)
Based on ”Geotechnical Terrain Class” classification (soil profile down to bedrock)
1) Buildings (incl. height etc), 2) Hard surfaces (road etc), 3) Green space (vegetation)
Terrain data (e.g. 2m raster); Soil geology
Based on Excel ’conditional matrix’ created by geotechnical engineering practise (reinforcement metod etc, distance between piles etc), calculated using a series of ArcGIS Models
Based on Excel ’condition matrix’, calculated using a series of ArcGIS Models
Geoteknik
GIS
Geotechics

## Slide 7
Type 1
Type 2
Type 3
50m
50m
Green space
Hard surface
Buildings
A development plan (’ready stage’) OR
modules of building blocks (’early stage’)

## Slide 8
Example of placement of modules and making consistent GIS-surfaces
*) consistent = adjacent, non-overlapping buildings; hard surfaces; green space

## Slide 9
Suggested reinforcement method

## Slide 10
Cost (for reinforcement) in Swedish Krona/m2 [2D display]
E.g. 1000 SEK ~ 100 US$

## Slide 11
Exaggerated height scale 1,5X
Cost (for reinforcement) in Swedish Krona/m2 [3D display in ArcScene]
~ 2 million US$
xls summary of TOTAL costs (tSEK)
Cut/fill
Reinforcement
Toxic cleanup
TOTAL
xls summary of cut/fill volumes (m3)
Cut
Fill
Steel, concrete or lime cement piles

## Slide 12
3D, top surfaces for various levels
GeoCost allows for zoning of height areas
Cut and fill [3D display]

## Slide 13
Two alternative locations for the same set of buildings…
Hemgården SV
Höjdzon: +5,9 m.ö.h.
Hemgården NO
Höjdzon: +8,4 m.ö.h.
Important calculation results:
Reinforcement costs in the Northeast would be double compared to the reinforcement cost if construcion would occur in Southwest.
TOTAL:
2 million US$
TOTAL:
4 million US$

## Slide 14
3D web display (with surrounding terrain and existing buildings) – ArcGIS Online/City Engine
https://gis.swedgeo.se/geokalkyl/3ws/
The tool (mxd, tbx, sxd, example data, Manual, instruction videos) is free to download at
http://gis.swedgeo.se/geokalkyl/verktyget
(in Swedish…)

## Slide 15
Thank you!
CONTACT
Mats Öberg (GIS-architect, M.Sc. Civil Engineering) Swedish Geotechnical Institute Hugo Grauers gata 5 B 412 96 GOTEBORG Phone: +46 709 730 129
E-mail: mats.oberg@swedgeo.se

## Slide 16
EXTRA

## Slide 17
GTK Geotechnical Terrain Class must be evaluated by geotechnical engineer
The soil profile to bedrock may vary considerably!

## Slide 18
Soil layer 1
Soil layer 2
Soil layer 3

## Slide 19
Item attributes may be shown

## Slide 20
A specific Geotechnical Terrain class
Load in kPa of a building
Reinforcement
depth
Various reinforcement metods applied
Conditional matrix
Developed by
A small part of one of the Models